## Slide 1: Inter-Integrated Circuit (I2C) Bus Interface AKA: Two Wire Interface (TWI)

## Slide 2: Brief History
Designed in 1982 by Philips Semiconductor (now NXP)
1992 - First public Spec released
Since 2006 no licensing fees are required
Widely adopted technology

## Slide 3: Why I2C?
Pins are precious!
  They take up space
  More pins  More expensive microcontrollers
  Adding pins is hard
    Might need a new microcontroller (if a larger, compatible one is available)
    Significant board changes
Performance is often not that important
So
  Use the minimum number of pins
  Run them at relatively low bit rates.

## Slide 4: Applications
Connecting to all kinds of small, slow peripherals
  Reading Configuration data from various devices (Memory, PCI cards)
  Accessing ADCs and DACs
  Reading from Real-time clocks
  Reading hardware monitoring devices (Fan speed, CPU Temperature, Accelerometers)
  Controlling power supplies for various system components
  GPIO expanders
  Many, many others

## Slide 5: I2C Bus Architecture
Two signals
  SCL – Serial Clock (used for coordination and timing)
  SDA – Serial Data (used for data and control signaling)
Up to 1008 peripherals
  1 or more “masters” that initiate communication on the bus
  Up to 127 “slaves” that masters communicate
Bit rates
  100 KHz (Standard mode)
  400 KHz (Fast Mode)
  3.4 MHz (High speed mode)
  1 MHz (Fast Mode Plus)
  5 MHz (Ultra fast mode)

## Slide 6: I2C Addressing
Each slave on an I2C bus has a unique address.
  Most use 7 bit addresses (we discuss this here)
  An extended 10-bit version also exists
The addresses usually fixed or only partially configurable
  E.g. Only the least-significant bit of the address for the IMU is settable. So you can only have two of these IMUs on one bus.
  Different devices will have different numbers of settable and fixed bits.
  You can’t mix components arbitrarily on the bus

## Slide 7: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Start

## Slide 8: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Address
R/W

## Slide 9: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Data

## Slide 10: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Stop