## Slide 1: I2C Bus Interface
Brandon Williams

## Slide 2: Brief History
Designed in 1982 by Philips Semiconductor (now NXP)
1992 - First public Spec released
Since 2006 no licensing fees are required
Widely adopted technology

## Slide 3: Applications
Reading Configuration data from various devices (Memory, PCI cards)
Accessing ADCs and DACs
Reading from Real-time clocks
Reading hardware monitoring devices (Fan speed, CPU Temperature, Accelerometers)
Controlling power supplies for various system components

## Slide 4: What is I2C?
NXP Overview Video:
http://www.youtube.com/watch?v=BcWixZcZ6JY

## Slide 5: Bus Specs
Only requires 2 wires
  SCL (Serial Clock)
  SDA (Serial Data)
Image from: http://www.robot-electronics.co.uk

## Slide 6: Bus Specs
Open Drain drivers
  SCL + SDA can only be driven low
  Use Pull-up resistors to pull high

## Slide 7: Masters and Slaves
Master
Slave
SCL
SDA
Masters
  Can initiate transfers
  Drives the SCL line
  Normally only one Master
Slave
  Can’t initiate transfers
  Respond to the Master
  Up to 100+ slaves per bus
Notes: Engineers have weird terms for everything. Masters and Slaves. Zombie children, Victim blocks, Evicting cache lines etc.

## Slide 8: I2C Protocol - Start/Stop
The Start/Stop sequences are the only times SDA can toggle while SCL is high
All other toggling of SDA must be done with SCL low

## Slide 9: I2C Protocol - Data
Data is sent in 8-bit transfers starting with the MSB
Followed by an ACK
  0 - Data received and ready for another Byte
  1 - Can’t receive any more data
Total of 9 clock cycles per transfer
SDA line must be valid while SCL is high

## Slide 10: I2C Protocol - Addressing
7-bits of Address
1-bit for Read/Write
  0 - Write
  1 - Read

## Slide 11: I2C Protocol - 10-bit Addressing
Extension to I2C allows 10-bits of Address
Requires two beats to specify Address
Sparkfun

## Slide 12: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Start

## Slide 13: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Address
R/W

## Slide 14: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Reg in Device
+
Data

## Slide 15: I2C Protocol - Full Xfer
Philips I2C Bus Specification
Stop

## Slide 16: I2C Repeated Start
Sparkfun

## Slide 17: I2C Speed
100 Kb/sec - Normal Operation
10 Kb/sec - Slow mode
400 Kb/sec to 3.4 Mb/sec - High Speed Modes

## Slide 18: Clock Stretching
Only Masters can send clock pulses
But Slaves can stretch the clock if needed
Slave stretching the clock
Clock

## Slide 19: Arduino Wire Library
begin()
requestFrom(Address, count)
beginTransmission(Address)
endTransmission()
send()
receive()

## Slide 20: Conclusion
Simple 2-wire bus
Master + up to 128 slaves