## Slide 1: Implementing PID

## Slide 2: To add
Discuss different ways they can control their quad
  Pitch/roll -> rate of change of angle
  Pitch/roll -> angle of attack
  Pitch/roll -> velocity
  Pitch/roll -> position
  Throttle -> throttle
  Throttle -> rate of climb
  Throttle -> altitude
Discuss higher-order control
  How to integrate GPS
  How to integrate barometer

## Slide 3: Note for Next Class
Demo
  Noise
  Noise reduction
  Complimentary filter.
  Integral windup
  Tuning PID
Control registers for IMU
  Register maps
  Writing registers
  Relationship between registers and circuit schematics of IMU internals
Combine this lecture with the flight control software lecture

## Slide 4: Control Theory
Making a physical system do what you want
“Open loop” and “closed loop”
Open loop - cannot see the system’s output
  Motor controllers
  LCD/LED/CRT screens
  Some ICBMs
Closed loop - Can see output, make corrections
  Autopilot
  GPS guided munitions
  Our quadcopter

## Slide 5: What is PID?
Make a system follow a set point
“Proportional, Integral, Derivative”
A brief history:
  1788 - James Watt’s flyball governor (P)
  1837 - Louis Molinié hydraulic regulator (PI)
  1857 - H.N. Throop marine engine governor (PD)
  1868 - Maxwell gives theoretical basis
  1911 - Elmer Sperry, ship steering (PID)

## Slide 6: Closed loop control
PID is the most common closed loop controller
Proportional: Directly against error
Integral: Remembers error over time
Derivative: Dampens response to avoid oscillations

## Slide 7: Example
https://sites.google.com/site/fpgaandco/pid

## Slide 8: PID on the Quadcopter
3 separate controllers
PID set point is from user

## Slide 9: Pitfalls of PID
Integral term “Windup”
  One solution: Exponential decay on integral (E.g., I = I/2 + error)
Derivative noise: beware of vibrations
Error term with vibration
Derivative term causes your system to go insane
  Solution: moving average of last several values. Or median of last several values.
  Using the serial plotter in arduino to watch the D term.
3. Tweaking PID values
Tune P first, then D, then I.

## Slide 10: Implementation
NOTES:
  Where to get the derivative?
  Integral windup
  Pay attention to rate (hz)
  Relative scale of inputs and outputs
    Should you include the time step?
    Make sure timestep is consistent

## Slide 11: How important in speed?
The key number is how many times/sec your PID loops (Hz)
The internet suggests > 100Hz (10ms/cycle) is necessary for stable flight.
My non-optimized code runs at 400Hz (2.5ms/cycles)
Action | Latency (ms)
Reading IMU | 7.360
analogWrite() | 0.012
analogRead() | 0.104
Integer PID (one channel) | 1.880 (531Hz)
FP PID (one channel) | 1.888 (529Hz)
AHRS getOrientation() | 1.860
rfWrite() 16 bytes | 0.812
Serial.write(“a”) | 0.906

## Slide 12: Remote Software Path
Scale gimbal readings (-512-512 for P,R, Y; 0-1023 for T)
“deadband” avoids noise near the mid point.
Performance is not critical 10-20Hz updates is more than enough.

## Slide 13: Quadcopter Datapath
Slow: Translate gimbal reads into ‘set points’
Fast: Use PID to track set points.
Add Filter to Diagram

## Slide 14: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
Pitch backward
  Less thrust to the rear
  More to the back

## Slide 15: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
Pitch Right
  More thrust to the left motor
  Less to the Right

## Slide 16: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW

## Slide 17: Some Possible Configurations
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6

## Slide 18: Maintaining Stability
Multi-rotor aircraft are inherently unstable
  Mismatched motor power (voltage variation, manufacturing variation in motors or props)
  Variation in air currents and density.
  Once perturbed, there’s no force acting on the aircraft to return it to equilibrium.

## Slide 19: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 20: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)