## Slide 1: Introduction To Eagle (and PCBs)

## Slide 2: PCBs are Made of Layers
Silkscreen – documentation labels
Metal – for making wires
Dialectric – insulation and structure
Solder mask – protective outer coating

## Slide 3: Metal Layers
The Metal layers for several components
  Conductive “traces” to connect components
  Pads for attaching/connecting components
N-layer boards have N metal layers
  N usually is 2,4,...
  Fewer layers  cheaper
Top and bottom layers are for mounting components and routing traces
Internal layers can serve several purposes
  Ground and power planes
  Other signal planes
  Internal routing layers

## Slide 4: Metal Layers (cont.)
Thickness is measured in oz per square foot.
Standard copper is 1oz
  About 0.034 mm
Thicker metal layers can carry more current

## Slide 5: Dielectric
The dielectric in the insulator between metal layers
Most PCBs use FR4
  “glass reinforced epoxy laminate”
  i.e., fancy fiberglass
  “FR” means “flame retardant”
Other specialized dielectrics are are available
  To support high speed circuits
  To manage thermal expansion

## Slide 6: Solder Mask
The solder masking is a polymer (plastic) coating on the top and bottom of the board
Solder does not adhere to it.
It serves several needs
  Protects the top and bottom metal from oxidation.
  Helps prevent solder bridges
Gives the board color
  FR4 is brown
  Solder mask comes in several colors.

## Slide 7: Silkscreen
It’s an opaque (usually) white epoxy or polymer
It provides documentation and markings
  References designators
  Part outlines
  Logos
  Serial numbers etc.

## Slide 8: Making Connections Between Layers
Plated holes connect metal layers.
  Drill a hole
  Electroplate it with copper
  If it’s exposed to air, plate it with a non-oxidizing metal.
Problems
  Takes up space in all layers
  Pins are generally pretty big
  Pin-to-pin spacing >= 1mm

## Slide 9: Pads and Vias
Through hole pads
  Mount devices with pins
  Sized for the pin + solder
  Always plated with non-oxidizing metal.
Vias are electrical connections
  As small as possible

## Slide 10: Surface Mount Devices (SMD)
No drill required
No pins
Smaller parts
Finer ‘pitch’ (pin-to-pin distance)
Parts on both sides
Easier automated placement
Pitch >= ~0.3 mm

## Slide 11: Lots of Choices, in Theory
There are many, many choices when designing a PCB
We will get to make very few of them
Cheap, fast PCB manufacturers provide a standard setup. E.g.:
  FR4
  1oz copper
  2 or 4 layers
  A few colors

## Slide 12: Steps for Designing PCBs
Create/acquire a library of components
Assemble your schematic
Lay out the board
Perform design checks
Generate CAM files
Check them carefully
Submit for manufacturing

## Slide 13: PCB Library
One Symbol
Many Packages
Many Parts

## Slide 14: The Library
Package
Symbol
Device Pin Mapping
Physical part

## Slide 15: Schematics

## Slide 16: Layout

## Slide 17: Schematic vs. Board

## Slide 18: Designing with Layers
Eagle (and other board design tools) use layers to specify different types of information about a board. E.g:
  Where wires should go on each physical layer
  Where wires should not go on each physical layer
  Documentation
  Mechanical information
Eagle defines 52 layers by default
‘t’ prefix means top.
‘b’ prefix means bottom (displayed mirrored)

## Slide 20: Eagle Layers
Top | Tracks, top side |  | 27 | tValues | Component VALUE, top side |  | 
Route2 | Inner layer |  | 28 | bValues | Component VALUE, bottom side |  | 
Route3 | Inner layer |  | 29 | tStop | Solder stop mask, top side (gen. autom.) |  | Design
Route4 | Inner layer |  | 30 | bStop | Solder stop mask, bottom side (gen. Autom.) |  | Documentation
Route5 | Inner layer |  | 31 | tCream | Solder cream, top side |  | Tool guidance
Route6 | Inner layer |  | 32 | bCream | Solder cream, bottom side |  | 
Route7 | Inner layer |  | 33 | tFinish | Finish, top side |  | 
Route8 | Inner layer |  | 34 | bFinish | Finish, bottom side |  | 
Route9 | Inner layer |  | 35 | tGlue | Glue mask, top side |  | 
Route10 | Inner layer |  | 36 | bGlue | Glue mask, bottom side |  | 
Route11 | Inner layer |  | 37 | tTest | Test and adjustment information, top side |  | 
Route12 | Inner layer |  | 38 | bTest | Test and adjustment inf., bottom side |  | 
Route13 | Inner layer |  | 39 | tKeepout | Restricted areas for components, top side |  | 
Route14 | Inner layer |  | 40 | bKeepout | Restricted areas for components, bottom s. |  | 
Route15 | Inner layer |  | 41 | tRestrict | Restricted areas for copper, top side |  | 
Bottom | Tracks, bottom side |  | 42 | bRestrict | Restricted areas for copper, bottom side |  | 
Pads | Pads (through-hole) |  | 43 | vRestrict | Restricted areas for vias |  | 
Vias | Vias (through all layers) |  | 44 | Drills | Conducting through-holes |  | 
Unrouted | Airlines (rubber bands) |  | 45 | Holes | Non-conducting holes |  | 
Dimension | Board outlines (circles for holes) |  | 46 | Milling | Milling |  | 
tPlace | Silk screen, top side |  | 47 | Measures | Measures |  | 
bPlace | Silk screen, bottom side |  | 48 | Document | Documentation |  | 
tOrigins | Origins, top side (generated autom.) |  | 49 | Reference | Reference marks |  | 
bOrigins | Origins, bottom side (generated autom.) |  | 51 | tDocu | Detailed top screen print |  | 
tNames | Service print, top side (component NAME) |  | 52 | bDocu | Detailed bottom screen print |  | 
bNames | Service print, bottom s. (component NAME) |  |  |  |  |  | 

## Slide 21: Useful Layer Commands
“display <layer>” -- show the layer
“display -<layer>” – hide the layer
“display last” return to previous view
Click and hold the layer tool icon to get a list of present layers sets.
  Select “new…” to save the current view
  Then “display foo” to switch to the view named “foo”

## Slide 22: Manufacturing
Eagle layers are partly Eagle-specific
  Some are semantic
  Some are documentary
Boards manufactures need
  Metal layers
  Silkscreen
  Soldermask
  Drills
  In a standard format

## Slide 23: Computer Aided Manufacturing (CAM) Files: Gerbers
Eagle’s CAM processor generates CAM files
  “Gerbers”
  “Drill file”
Manufacturing Reqs
  Minimum drill size
  Minimum feature width
  File formats
Our manufacturer
  https://jlcpcb.com/capabilities/Capabilities
Our configuration
  QuadClass-Resources/Eagle/DRU/*
  QuadClass-Resources/Eagle/CAM/*

## Slide 24: The Lab
Use Eagle to design a simple schematic and board.
Run it through the tool flow.
Submit it through Eaglint

## Slide 25: Eagle Lint
lint:
  Tool to check coding standards and other invariants about a system.
Eaglint will check your libraries, schematics
  Check for correctness
  Check for style
Also checks for other files in your repo
  Eaglint will tell you what it’s looking for.
  Pay attention.
Provides a workflow for me to review your designs and provide feedback.
To use
  Visit http://eaglint.nvsl.io
  You received a welcome email a couple of nights ago.

## Slide 26: Eagle Lint Process
Commit and push your changes to github
Submit your repo to Eaglint for a quick check
Submit your repo to Eaglint for a full check
If warnings/errors
  Fix and goto 1.
Submit for human review
If rejected
  Read comments; goto 1.
Else if accepted
  Goto next lab

## Slide 27: Grading on PCB Labs
The key to PCB design is attention to detail.
  Building a real board can take 4 months.
  If you make a mistake, it takes 4 months to fix.
    Contrast to software: just recompile and rerun!
  Don’t make any mistakes! Check your work!
Grading for PCB labs
  A “perfect” score is 20 points
  You start out with 22-24 points (depending on the lab).
  Every time you submit a design to Eaglint, you lose 1 point.
  Every time you submit a design for human review Eaglint, you lose 1 point.
  You must complete the labs.
”Quick checks” are free.

## Slide 28: Resources
Good PCB manufacturing videos
  https://www.youtube.com/playlist?list=PL8zP8UuDk8a0ZNWiteC-7PHx1HCeBY0qB