## Slide 1: Sensing and Filtering

## Slide 2: Principles of Operation (1)
Z
Y
X
An even number of motors provides lift and control in 6 dimensions
  Spatial dimensions: x, y, z
  Pitch: rotation around left-right (y) axis
  Roll: rotation around the front-back (x) axis
  Yaw: rotation around the top-bottom (z) axis
A flight computer operates a closed-loop controller to maintain stability and implement pilot commands.

## Slide 3: Maintaining Stability
Multi-rotor aircraft are inherently unstable
  Mismatched motor power (voltage variation, manufacturing variation in motors or props)
  Variation in air currents and density.
  Once perturbed, there’s no force acting on the aircraft to return it to equilibrium.

## Slide 4: Lab Tasks
Read values from IMU.
Use Arduino’s plotting tool
Run your serial port at max speed!!!
Read the pitch of your test stand with the motors on
  Configure the filters on the IMU
  Implement a complimentary filter in software.

## Slide 5: Euler Angles
3 angles to specify an orientation
The AHRS library gives you the pitch and roll angles
We don’t need the yaw angle

## Slide 6: Accelerometer
Measure forces acting on the quadcopter (mostly gravity)
Some trigonometry will yield Euler angles
Strengths
  No drift
  Good low-frequency performance
Weakness
  Susceptible to vibration
  Poor high-frequency performance

## Slide 7: Computing Euler Angles

## Slide 8: Gyroscope
Measure rate of for Euler angles
Integrating will give you Euler angles
Strength
  Less susceptible to noise
  Good high-frequency performance
Weakness
  The integral will drift
  Poor low-frequency performance

## Slide 9: Accelerometer Noise

## Slide 10: Gyroscope Noise

## Slide 11: Gyro Clipping
Clipping occurs when the measured value exceed what the IMU can measure
Since we are integrating the gyroscope, clipping is especially bad.

## Slide 12: Gyro Clipping

## Slide 13: Filtering
High frequency vs. low frequency
High-pass filters
Low-pass filters

## Slide 14: IMU Internal Accelerometer Filter

## Slide 15: Hardware Registers
Configuration variables for a piece of hardware

## Slide 19: I2C Peripherals

## Slide 21: Accelerometer Datapath

## Slide 22: Gyroscope Datapath

## Slide 23: Filter Example

## Slide 24: Complimentary Filter
Combine the best of accelerometer and gyro
  High-frequency from the gyroscope
  Low frequency from the accelerometer
The math is pretty simple
    θnew the new estimated Euler angle
    Θold the previous estimated Eurler angle
    dθ/dt gyro measurement
    Δt Time since last gyro measurement
    θe Euler angle from the accelerometer
    C The “complimentary gain”
θnew = C*(θold + Δt*dθ/dt ) + (1-C)*θe

## Slide 25: Tuning
Two goals
  Low noise
  Low lag

## Slide 29: Quadcopter Datapath
Use complimentary filter to blend acc. And gyro data
  Pitch and roll
  Complimentary gain should come from the remotse

## Slide 30: The PID Controller

## Slide 31: To add
Discuss different ways they can control their quad
  Pitch/roll -> rate of change of angle
  Pitch/roll -> angle of attack
  Pitch/roll -> velocity
  Pitch/roll -> position
  Throttle -> throttle
  Throttle -> rate of climb
  Throttle -> altitude
Discuss higher-order control
  How to integrate GPS
  How to integrate barometer

## Slide 32: Note for Next Class
Demo
  Integral windup
  Tuning PID
Combine this lecture with the flight control software lecture

## Slide 33: Control Theory
Making a physical system do what you want
“Open loop” and “closed loop”
Open loop - cannot see the system’s output
  Motor controllers
  LCD/LED/CRT screens
Closed loop - Can see output, make corrections
  Autopilot
  GPS guided munitions
  Our quadcopter

## Slide 34: What is PID?
Make a system follow a set point
“Proportional, Integral, Derivative”
A brief history:
  1788 - James Watt’s flyball governor (P)
  1837 - Louis Molinié hydraulic regulator (PI)
  1857 - H.N. Throop marine engine governor (PD)
  1868 - Maxwell gives theoretical basis
  1911 - Elmer Sperry, ship steering (PID)

## Slide 35: Closed loop control
PID is the most common closed loop controller
Proportional: Directly against error
Integral: Remembers error over time
Derivative: Dampens response to avoid oscillations

## Slide 36: Example
https://sites.google.com/site/fpgaandco/pid

## Slide 37: PID on the Quadcopter
3 separate controllers
PID set point is from user

## Slide 38: Pitfalls of PID
Integral term “Windup”
  One solution: Exponential decay on integral (E.g., I = I/2 + error)
Derivative noise: beware of noise.
Error term with vibration
Derivative term causes your system to go insane
  Solution: moving average of last several values. Or median of last several values.
  Using the serial plotter in arduino to watch the D term.
3. Tweaking PID values
Tune P first, then D, then I.

## Slide 39: Implementation
NOTES:
  Where to get the derivative?
  Integral windup
  Pay attention to rate (hz)
  Relative scale of inputs and outputs
    Make sure timestep is consistent

## Slide 40: How important in speed?
The key number is how many times/sec your PID loops (Hz)
The internet suggests > 100Hz (10ms/cycle) is necessary for stable flight.
My non-optimized code runs at 400Hz (2.5ms/cycles)
Action | Latency (ms)
Reading IMU | 7.360
analogWrite() | 0.012
analogRead() | 0.104
Integer PID (one channel) | 1.880 (531Hz)
FP PID (one channel) | 1.888 (529Hz)
AHRS getOrientation() | 1.860
rfWrite() 16 bytes | 0.812
Serial.write(“a”) | 0.906

## Slide 41: Maintaining Stability
Multi-rotor aircraft require a closed loop controller
  Sensors detect aircraft movement and orientation
  Controller adjusts the power to motors to maintain desired location and orientation
Multi-rotor aircraft use a few sensors to maintain stability
  Accelerometers (absolute pitch and roll)
  Gyroscopes (changes in pitch, roll, and yaw)
The flight computer implements the control algorithm
  Usually a proportional, integral, derivative (PID) controller implemented in software.
  We will talk more about this later.
With PID controllers for pitch, yaw, and roll multirotor aircraft can achieve stable flight.

## Slide 42: Tuning
Tuning PID is a bit of an art form.
Simple algorithm
  Set P=I=D = 0
  Increase P until it starts oscillating, reduce until it oscillates just a bit
  Increase D to till it stabilizes pretty quickly
  Increase I to fix offset
  Increase D as much as possible with causing oscillation.

## Slide 43: Tuning
Zeigler-Nichols method.
  P=I=D= 0
  Increase P until oscillations start. P is now at Ku, oscillation is at frequency Tu.
  Follow the chart.
  It’s important that your PID look incorporate its execution interval correctly.

## Slide 44: Slides on Sensors
Accelerometer
  Demo the data we get (3-axis accelerations)
  Conversion to Euler angles. Show math.
  Conversion to acceleration along x,y,z?
  Maybe talk about coordinate systems?
Gyroscope
  Demo the data we get
Other sensors
  GPS
  Barometer
  Magnetometer
  Temperature (for correcting measurements)
    https://wiki.dronecode.org/_media/u01.imu_temperature_compensation_-_hessel_van_der_molen.pdf

## Slide 45: New Slides on Filters
Noise
Calibration
Demo of noisy measurements
Demo of progressive improvements
  Calibration
  Tuning filters in the quadcopter
  Tuning complimentary filter
    Demo Drift from integrating gyroscope
  Tuning moving average on euler angles
Demo of “good” pitch/roll angle measurements
Discuss magnetometer?
  Calibration: https://github.com/kriswiner/MPU-6050/wiki/Simple-and-Effective-Magnetometer-Calibration
  Heading calculations

## Slide 46: Higher-order Navigation
Large multi-rotor aircraft can do more
  Maintain geographic position
  Maintain altitude
  Follow an prescribed/pre-programmed path
More sensors required
  Magnetometers (absolute yaw or heading)
  GPS (absolute location and altitude)
  Barometers (altitude)

## Slide 47: Controlling Pitch
Pitch forward
  More thrust to the rear
  Less to the front
Pitch backward
  Less thrust to the rear
  More to the back

## Slide 48: Controlling Roll
Pitch Left
  More thrust to the right motor
  Less to the left
Pitch Right
  More thrust to the left motor
  Less to the Right

## Slide 49: Controlling Yaw
Rotate CCW
  More thrust to the CCW motors
  Less to the CW
Rotate CW
  More thrust CW motors
  Less to the CCW

## Slide 50: Some Possible Configurations
“Plus”
“X”
“Octothorpe”
Hexa +
Hexa x
Octa +
Octa x
Y 6